## Slide 1: Concept Presentation for the Bachelor Thesis on The Biogas Potential of Sewage Sludge, Fermentation Residue, and Cow Manure
Alexandra Erfort
Environmental Engineering BSc, TU Berlin
17.05.2018

## Slide 2: Outline
Introduction
Objective
Hypotheses
Materials and Methods
Expected Results
Time Schedule
Sources

## Slide 3
Research in context of the BioRist project:
Necessary data for current research regarding optimization of biogas yield from water hyacinths with rice straw and cow manure
Search for co-substrates to optimize the biogas yield in the pilot plant in Vietnam
Preparation for batch experiments
Need for a supplement for rice straw
Biogas potential of the inoculum on its own
1. Introduction

## Slide 4
Inocula:
1. Introduction
Cow manure
Sewage sludge
Fermentation residue
“Cow excreta used as fertilizer” [1]
“Product of wastewater treatment […] solid wastes are separated from the liquid wastes through settling […] processed and […] decomposed by bacteria” [2]
“Sludge or thickened mixture of sewage solids with water that has been decomposed by anaerobic bacteria” [3]

## Slide 5
  Compare biogas potential of sewage sludge, fermentation residue, and screened & unscreened cow manure
  Calculate the standard liters
  Investigate the effects of not stirring a substrate during incubation
  Create a guideline on how to implement this type of experiment in the institute’s laboratory
  Based on the VDI 4630
  Include a thorough error analysis
2. Objective

## Slide 6
Limited growth for all substrates and most growth within the first week of incubation
Original (unscreened) cow manure has a higher biogas yield than screened cow manure
3. Hypotheses

## Slide 7
Analyzed parameters: Dry matter, ignition loss and C/N (?)
  Before and after incubation
Degassing with nitrogen  anaerobic environment
Incubation under mesophilic conditions (37 °C ± 2 °C) [5]
OxiTop one measurement every hour for two weeks
4. Materials and Methods

## Slide 8
Limitations:
Magnetic Stirring Table
  Limited to only six bottles simultaneously
  Space for only two tests, since at least triple determinations should be conducted [5]
Maximum pressure for gas meter
  Manual pressure release necessary
4. Materials and Methods
Notes:  especially in beginning need to release pressure

## Slide 9
4. Materials and Methods
OxiTop Measuring Head
Inoculum
OxiTop Controller
Pressure Release
Stirring Flea

## Slide 10
Inocula:
4. Materials and Methods
Cow manure
Sewage sludge
Fermentation residue
Fresh and stored
Screened and unscreened
Stirred and unstirred

## Slide 11
4. Materials and Methods
Experiment | Inoculum |  | 
1st 2 weeks | 3x sewage sludge | 2x sewage sludge + 1 g cellulose | 1x sewage sludge + 2 g cellulose
2nd 2 weeks | 3x cow manure | 3x screened cow manure | 
3rd 2 weeks | 3x sewage sludge (4 weeks old) |  | 
4th 3 weeks | 3x fermentation residue | 3x fermentation residue, unstirred | 
Notes: After 2 days took cellulose ones out of incubator over night and cancelled them completely after 5 days

## Slide 12
Reasons for not-stirring:
Too much stirring might inhibit microorganisms and cause a drop of methane production [6]
Without active stirring, still slight mixing due to thermal convection flows and rising gas bubbles [7]
In general: short-term intensive stirring is more effective than long-term weak stirring [7]
4. Materials and Methods
Notes: Usually not enough in biogas plants but may be enough for the small amounts we use in the lab

## Slide 13
5. Expected Results
time
pressure

## Slide 14
6. Time Schedule
 | April |  |  |  | May |  | June |  | July |  | August | Septem-ber | 
Literature research |  |  |  |  |  |  |  |  |  |  |  |  | 
Experiments |  |  |  |  |  |  |  |  |  |  |  |  | 
Data analysis |  |  |  |  |  |  |  |  |  |  |  |  | 
Interim Presentation |  |  |  |  |  |  | x |  |  |  |  |  | 
Writing |  |  |  |  |  |  |  |  |  |  |  |  | 
Final Presentation |  |  |  |  |  |  |  |  |  |  |  |  | 
Today
x

## Slide 15
[1] | The Free Dictionary: Cow Manure. N.Y. [Access: 10.05.2018: https://www.thefreedictionary.com/cow+manure]
[2] | Center for Food Safety: What is Sewage Sludge? N.Y. [Access: 10.05.2018: https://www.centerforfoodsafety.org/issues/1050/sewage-sludge/what-is-sewage-sludge]
[3] | The Free Dictionary: Digested Sludge. N.Y. [Access: 10.05.2018: https://encyclopedia2.thefreedictionary.com/digested+sludge]
[4] | R. Zhang; H. El-Mashad: Biogas production from co-digestion of dairy manure and food waste. 2006. [Access: 09.05.2018: https://www.sciencedirect.com/science/article/pii/S0960852410000842]
[5] | Verein Deutscher Ingenieure: VDI 4630. 2016.
7. Sources

## Slide 16
Sources
[6] | R. Kliche; M. Lebuhn: Bayern Biogas Forum: Schaum in Biogasanlagen. 2017. [Access: 09.05.2018. http://www.biogas-forum-bayern.de/media/files/0003/schaum-in-biogasanlagen.pdf].
[7] | H. Klußmann: Pump- und Rührtechnik in landwirtschaftlichen Biogasanlagen. N.Y. [Access: 09.05.2018. http://www.bfl-online.de/media/pump_und_%20ruehrtechnik_in_%20biogasanlagen.pdf].
[8] | Browne, J. et al.: The effects of storage time and temperature on biogas production from dairy cow slurry. 2014. [Access: 09.05.2018: https://ac.els-cdn.com/S1537511014001615/1-s2.0-S1537511014001615-main.pdf?_tid=d89c68a7-4800-489d-9c15-b92e3fc6d42e&acdnat=1525898666_12a46d6ec82740a8b5f6b48d10a99962]
Image source from slides 4, 5, 9 and 10: flaticon.com

## Slide 17: Thank you for your attention! Any questions?

## Slide 18: Additional Slides

## Slide 19
Experimental Setup

## Slide 20
No studies on the comparison of stirred and not-stirred
No studies on the comparison of fresh and stored sewage sludge
  Only on slurry, where it had almost no effect [8]
Not a lot on the effects of screening the manure
  “Based on mass balance calculations, separation of the coarse fraction of manure would sacrifice about 32 % of the energy potential” [4]
What is new?

## Slide 21
Order of biogas yield for the different substrates:
  Original Cow Manure > Screened Cow Manure > Fermentation Residue = Unstirred Fermentation Residue > Fresh Sewage Sludge > Stored Sewage Sludge
Not-stirred substrate is similar to stirred substrate regarding the yield of biogas
Further Hypotheses

## Slide 22
First Results
Chart: Comparison of sewage sludge biogas production from three bottles

## Slide 23
First Results
 | TS | oTS
Pre-incubation | 2.1 % | 63.6 %
Post-incubation | 2.0 % | 60.3 %

## Slide 24
Introduction
  Motivation
  Goal & hypotheses
Background
  Biogas: anaerobic digestion
  Sewage sludge, fermentation residue and cow manure
  VDI 4630
Material
  Sewage Sludge (fresh, stored)
  Fermentation Residue (stirred, not stirred)
  Cow Manure (screened, unscreened)
Methods
  Literature research
  Substrates analyses
    Dry matter
    Ignition loss
    C, N, S
  Instructions for incubation according to VDI 4630
Results
  Literature results
  Substrate Parameters
  Incubation results
    Resulting Biogas production rate
    Comparison of different inocula
      Sewage sludge: fresh and stored
      Fermentation residue: stirred and not stirred
      Cow manure: screened and not screened
Discussion
  Biogas production rate
    Comparison of all six different inocula
  VDI 4630
  Error analysis
Conclusion
  Hypotheses answered?
  Further Research Demand
  Practicability for Vietnam
Outline for Thesis