## Slide 1: Biogas Potential of the Inocula Sewage Sludge, Cow Manure, and Fermentation Residues – Investigation of Varying Pre-Treatment and Process Options
Bachelor Thesis
Final Presentation
31st July, 2018
Alexandra Erfort

## Slide 2: Outline
Motivation
Objectives
Hypotheses
Methods
Results
Discussion
Conclusion

## Slide 3: Motivation
Research in context of the BioRist project
Biogas pilot plant in Vietnam
  Inoculum: Cow manure
Search for co-substrates
Data on inoculum required
Extended with sewage sludge and fermentation residues
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion

## Slide 4: Objectives
  Compare gas-formation potential of the inocula
  During incubation period of two weeks
  Investigate effects of varying pre-treatment and process options
Fresh and stored
Screened and unscreened
Stirred and unstirred
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion

## Slide 5: Hypotheses
Restricted Logistic Activity [1]
Minimal Effect of Storage [2]
Screening Increases Gas Yield [3]
Little Effect of Stirring [4; 5; 6]
p
t
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion

## Slide 6: Methods
OxiTop measuring system
Flushed with N2 for anaerobic environment
Placed in climatic chamber at 37°C
Maximum pressure  manual pressure releases
Analyzed parameters:
  Dry substance
  Organic dry substance
  C/N ratio
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion
Notes: max. 230 hPa increase

## Slide 7: Results – Sewage Sludge
Chart: Comparison Fresh Vs. Stored Sewage Sludge
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion
Notes: Fast increases correlate with pressure releases  temperature fluctuations
Restricted

## Slide 8: Results – Cow Manure
Chart: Comparison Unscreened Vs. Screened Cow Manure
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion
Notes: Restricted and linear; screened extended

## Slide 9: Results – Fermentation Residues
Chart: Comparison Stirred Vs. Unstirred Fermentation Residues
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion
Notes: First restricted, then linear, extended

## Slide 10: Results – Overall Comparison
Chart: Comparison of Biogas Potential from the Inocula Under Varying Conditions
| 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | Fresh Sewage Sludge | Stored Sewage Sludge | Unscreened Cow Manure | Screened Cow Manure | Stirred Fermentation Residues | Unstirred Fermentation Residues
Two Weeks | 249.5467 | 218.7424 | 243.1652 | 81.0389 | 86.9122 | 80.3612 | 51.8606 | 55.4703 | 51.1088 | 201.7802 | 115.3372 | 218.1755 | 76.7845 | 82.7934 | 94.2936 | 63.9408 | 69.8592 | 77.5217
Additional Two Weeks | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 519.388 | 531.753 | 389.0623 | 82.306 | 82.9208 | 82.6254 | 57.8772 | 67.8512 | 86.6107
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion
Notes: Biogas potential expressed as NL/kg oDS  better comparability
No correlation between oDS degradation and C/N ratios

## Slide 11: Discussion
Restricted Logistic Activity
  Restricted due to limited resources
Minimal Effect of Storage
  High loss of potential during storage
Screening Increases Gas Yield
  Smaller particles more accessible for microorganisms
Little Effect of Stirring
  Stirring of little amounts not necessary to release gas
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion

## Slide 12: Discussion
Temperature fluctuations cause simulated biogas volume
Continuous stirring and changes in temperature might inhibit microorganisms [7]
Observations of produced volume and organic dry substance and C/N ratios do not show correlations
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion

## Slide 13: Discussion – Practicability for Vietnam
Laboratory provides different conditions than present on site
No easy storage without sacrificing big percentage of biogas potential
Screening cow manure increases biogas potential significantly
Due to larger scale in biogas plant substrates must be mixed
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion

## Slide 14: Conclusion
Material should be fresh, have small particles, and be stirred regularly for highest biogas potential.
Further Research Demand:
Correlation between biogas yield and organic substance degradation and C/N ratios
Effects of temperature fluctuations on biogas yield
Motivation - Objectives - Hypotheses - Methods - Results - Discussion - Conclusion

## Slide 15: References
[1] | Helmich, U.: Logistisches Wachstum. Helmichs Biologie-Lexikon. 2016. [http://www.u-helmich.de/bio/lexikon/L/logistisches_Wachstum.html], Access: 24.05.2018.
[2] | Browne, J.D.; Gilkinson, S.R.; Frost, J.P.: Biosystems Engineering: The effects of storage time and temperature on biogas production from dairy cow slurry. Vol. 129, Amsterdam: Elsevier, 2014 .
[3] | Mshandete, A.; Björnsson, L.; Kivaisi, A.K.; Rubindamayugi, M.S.T., Mattiasson, B.: Renewable Energy: Effect of particle size on biogas yield from sisal fibre waste. Vol. 31, Amsterdam: Elsevier, 2006.
[4] | Kliche, R.; Lebuhn, M.: Schaum in Biogasanlagen. Biogas Forum Bayern, 2017. [http://www.biogas-forum-bayern.de/media/files/0003/schaum-in-biogasanlagen.pdf], Access: 09.05.2018.
[5] | Schieder, D.; Gronauer, A.; Lebuhn, M.; Bayer, K.; Beck, J.; Hiepp, G.; Binder, S.: Prozessmodell Biogas. Biogas Forum Bayern, 2010. [http://www.biogas-forum-bayern.de/media/files/0001/Prozessmodell-Biogas.pdf] Access: 24.05.2018.

## Slide 16: References
[6] | Klußmann, H.: Pump- und Rührtechnik in landwirtschaftlichen Biogasanlagen. n.s. [http://www.bfl-online.de/media/pump_und_%20ruehrtechnik_in_%20biogasanlagen.pdf], Access: 09.05.2018.
[7] | Spahr, M.: Personal communication. Herbst Umwelttechnik GmbH, 27.06.2018.
Image source from slides 3, 4, 5, 11, 13, 14, 17, 18, 20, and 21: flaticon.com

## Slide 17
Thank you for your attention!
Any questions?

## Slide 18: Additional Slides – Volume Calculation
VBiogas Δp Vhead Vm R T | Biogas volume Absolute pressure difference Volume of the head space Molar volume Universal gas constant Absolute temperature

## Slide 19: Additional Slides – Limitations
Magnetic Stirring Table
  Limited to only six bottles simultaneously
  Space for only two tests, since at least triple determinations should be conducted
Maximum pressure for measuring heads
  Manual pressure release necessary

## Slide 20: Additional Slides – oDS and C/N Ratios
Inoculum | ΔoDS [%] |  |  | ΔC/N Ratio |  | 
 | 1 | 2 | 3 | 1 | 2 | 3
Fresh SS | 4.41 | 4.4 | 4.48 | -0.69 |  | 
Stored SS | 1.01 | 0.38 | 0.43 | -0.54 | -0.74 | -0.59
Unscreened CM | 2.66 | 3.29 | 4.77 | -3.95 | -0.03 | -0.07
Screened CM | 3.69 | 2.42 | 2.35 | -1.13 | -2.12 | -1.03
Stirred FS | 4.62 | 4.24 | 4.69 | -1.68 | -1.65 | -1.4
Unstirred FS | 3.89 | 2.28 | 2.81 | 0.49 | 0.4 | 0.59
Medium
High
Low
Biogas Yield (NL):
Notes: oDS and CN, differences from before and after incubation, since before the values were all the same  no correlation to highest or lowest yield
Unstirred FR only inoculum where C/N increased during incubation

## Slide 21: Additional Slides – Corrected Volumes
Chart: Comparison of Measured and Corrected Average Volumes
| Fresh SS | Stored SS | Unscreened CM | Screened CM | Stirred FR | Unstirred FR
Measured | 237.1533 | 82.77 | 52.8133 | 658.5 | 167.24 | 141.22
Corrected | 220.5933 | 77.3533 | 49.0433 | 625.2633 | 154.4167 | 128.1933
Notes: Due to temperature fluctuations big error, on average 8% added through simulated biogas

## Slide 22: Additional Slides – Material
OxiTop Measuring Head
Inoculum
OxiTop Controller
Pressure Release
Stirring Flea

## Slide 23: Additional Slides – Results
Overall biogas potential after two weeks:
Fresh
Screened
Stirred
Stored
Unscreened
Unstirred
>
>
>
>
>